# FPS PNEUMATIC SPECIALIST REVIEW PRE-TEST #2

REV. 8-2014

1. An air-oil intensifier with a single acting cylinder having a 3” diameter piston and a 3” stroke,

(spring returned force has a maximum of 25 pounds), powers an oil piston intensifier with a

.5” bore. How many SCFM of air is required to deliver ½ GPM at a pressure of 4000 PSIG?

Answer _________________

2. If a bulb had 50 ohms of resistance and 120-volt supply, what wattage would the bulb have?

Answer _________________

3. A pulse width modulated (PWD) signal controls down stream pressure. Supply pressure is

100PSIG. If 10% signal begins to open a regulator and 80% signal is wide open, what would

the pressure be down stream with a 60% signal?

Answer _________________

4. What size compressor (SCFM) would be needed to cycle a 4” bore, double acting cylinder with

a 1” rod that has a 12” stroke 45 times a minute?  Supply pressure is 105PSIG.

Answer _________________

5. What size receiver is needed to supply 2.0 CFM of air between 100 PSIG and 80 PSIG

for 2 minutes.   Temperature remains constant.

Answer _________________

6. A compressor on a 100 gal receiver supplies 10 SCFM at 120 PSIG. How long will a demand

of 15 SCFM last if 90 PSIG turns the system off?

Answer _________________

7. What is the Kinetic energy of a box that weighs 50 pounds, sliding down a 20-foot conveyor

in 3 seconds?

Answer ____________IN-LB

8. What would 15 Microns of Hg measure in Inches of Hg?

Answer _________________

9. A 15” stroke cylinder is equipped with a digital linear transducer with a 10-bit output.

What is the resolution?

Answer _________________

10. What size SCFM compressor operating at 80% duty cycle would be required to supply

1-CFM at 90 PSIG?

Answer _________________

# REVIEW PRE-TEST #2  ANSWERS

REV. 8-2014

REV. 7-2015

OK 12-2015

1.  21.17 SCFM

2.  288 Watts

3.  71.43 PSIG

4.  61.94 SCFM

5.  156.5 GAL

6.  5.46 minutes

7.  1656 IN-LB

8.  .00059055 inches

9.  .01465 inches

10. 8.9 SCFM